## Slide 2: GOCPI
A Scalable Energy Modelling Solution
Developed by Connor McDowall
Supervised by Rosalind Archer

## Slide 3: Facing the Energy Transition
The imminence of the energy transition is clear after working at ExxonMobil Australia.
Literature review informs the need for rapid transformation as economic models predict unfavourable consequences if no swift action.
Sustainable investment is driven by Net Present Value (NPV) analysis and the ability to generate returns for investors.
Sustainable technologies have seen significant cost reductions over the last decade improving the feasibility of the transition.
However, there are educational disparities between policy makers, government, private companies, stakeholders and voters.

## Slide 4: Empower users to influence policy
The reasons creating these issues is the sophistication and inaccessibility of energy modelling.
Energy modelling usually requires:
  Proprietary data.
  The understanding of LP, Integer LP, MIP and/or NLP optimisation techniques.
  Access to expensive commercial solvers.
  A thorough understanding of energy systems, mathematics, economics and finance.
This complexity creates difficulties in evaluating energy investment, policy and their alignment to the United Nation’s Sustainable Development Goals and Paris Agreements.
My proposed solution is to develop an accessible, scalable energy system modelling tool.
The product will remove this sophistication and enable users to model their own energy systems to inform investment and policy.

## Slide 5: Methodology and Implementation
A comprehensive literature review on energy, emissions, the economy, policy, obstacles, challenges and energy modelling framed the problem and addressed the product needs.
A high-level overview of the methods and implementation for the GOCPI project follows:
  Adapt The Integrated Markel E-Form System (TIMES) modelling methodology.
  Adapt the OseMOSYS modelling methodology.
  Understand and create energy systems.
  Develop a Python-based open source scalable energy modelling tool.
  Develop forecasting methodologies for energy systems.
  Adapt IBM technologies to facilitate optimisation.
  Develop an web-based user interface to both inform and distribute the product.

## Slide 6: The Incumbent’s Limitations – TIMES
The Integrated Markel E-Form System (TIMES) is the legacy methodology used to inform the energy scenarios for both the World Energy Council and New Zealand Business Energy Council.
A existing modelling system was adapted using enterprise versions of GAMS Studio and the Versatile Data Analyst (VEDA).
Excel-based functions and custom macros were to be used to create a scalable template.
Reproducibility, integration and complexity issues led to the abandonment of this approach in favour of an alternative.

## Slide 7: Discovering an Alternative – OseMOSYS
The Open Source Energy Modelling System (OseMOSYS) was the chosen alternative for modelling energy systems.
OseMOSYS is developed by a community of developers who make contributions directly to the OseMOSYS GitHub Repository. There are a couple versions available: GAMS, GNU Mathprog and Python.
OseMOSYS is a linear optimisation problem describing an energy system. There are 11 sets, 52 parameters, 67 variables, 94 constraints and 1 objective function.
Several sets underpin parameters, constraints and variables: Year, Technology, Timeslice, Fuel, Emission, Mode of Operation, Region, Season, Day Type, Daily Time Bracket and Storage.

## Slide 8: Breaking Down Energy Systems
A reference energy system underpins the system. It describes the network flows amongst the production, conversion and consumption of different fuels using different technologies.
The system models trade relationships between regions. Individuals, companies, towns, cities, countries and continents are examples of all regions you can represent using the OseMOSYS methodology.
The objective function minimises total discounted costs derived by each regions’ discount rate. Salvage, operating and capital expenditure are considered with the discount rate depending a region’s mix of equity, debt and financing costs.
The OseMOSYS model uses emissions and renewable technology constraints to drive sustainable outcomes.

## Slide 9: A Powerful Package
The GOCPI prototype was developed and distributed as a Python-based open source scalable energy modelling tool.
GOCPI required best practise software development. The project made use of several technologies: Version control using Git and GitHub, Python 3.7.6, Anaconda, PyPI, IBM ILOG CPLEX Optimization Studio (CPLEX Python APIs), IBM Watson Machine Learning and Yapf.
The model is an adaptation of the OseMOSYS methodology, formulated in GNU Mathprog and integrated into Excel and Python. The GNU Mathprog structure is stored within an Excel spreadsheet. A user may toggle constraints or adapt the objective function to drive different outcomes.
The prototype enables the user to formulate their own energy systems in python, perform forecasting functionalities, generate linear programmes and solve them using commercial solvers.

## Slide 10: Intersecting Technology, Energy & Finance
The GOCPI saw the intersection of technology, energy and finance in the construction of energy systems.
Deconstructed the Utopian energy system exemplar from OseMOSYS to formulate standardised modelling approach.
Partially developed an Australia/New Zealand energy system with a bi-lateral trade relationship.
Developed a reference energy system for both countries using data available from the Ministry of Business, Innovation and Education (MBIE, NZ) and the Department of Environment and Energy (AUS).
Determined discount rates for both New Zealand and Australia using treasury reports and financial statements.

## Slide 11: Programming the Foundations
The GOCPI prototype is built with several classes.
EnergySystems: A class containing modules to load in existing energy systems. Additionally, this class creates energy model files from the OseMOSYS structure and energy data files to form LP files.
CreateCases: A class containing modules to enable the user to build their own energy systems.
Forecasting: A class containing modules to formulate base year energy balances from the International Energy Agency’s (IEA) energy balances and forecast both energy and financial values.
Optimisation: A class containing modules to solve energy system optimisation problems locally using CPLEX or remotely using the IBM Watson Machine Learning service.
Navigation: A class containing modules to enable the user to navigate their local directory to access files.

## Slide 12: Driving Optimisation with IBM
CPLEX was selected as the commercial solver of choice for the GOCPI prototype. It is readily available for educational institutions and individuals using IBM’s Academic Initiative.
IBM ILOG Optimisation Studio was installed locally using the IBM Academic Initiative.
LP files are created using the glpsol terminal command, from the GLPK package, in a custom python environment.
Small LP files are solved locally using the CPLEX APIs accessible from the Optimisation class.
Large LP files must be solved using a Python-based OseMOSYS formulation and the IBM Decision Optimisation on the IBM Watson Machine Learning service.
Created a standardised method to access IBM cloud services, create deployments, request jobs and solve requests.

## Slide 13: Distributable on the GOCPI Interface
The package is distributed on PyPI and GitHub, accessible through a web-based interface (https://connormcdowall.com)
Developed a GitHub repository to version control all code and resources.
Developed a custom Python package for deployment. New distribution are uploaded using Twine and downloaded using Pip, Python’s package management software.
Developed a website to act as an interface for the GOCPI prototype. The website is built using Jekyll, a simple static site generator. Jekyll is written in Ruby and converts Markdown files to HTML. The website is hosted using GitHub pages.
Enabled a Google domain to direct a user to the interface. The website displays this presentation and will include links needed to access the GOCPI prototype.

## Slide 14: Success So Far
The GOCPI Prototype is readily available and distributable.
Created a standardised modelling process to create user-defined energy systems.
Partially developed an Australia and New Zealand energy system with a bi-directional trade relationship.
Created 80+ new distributions for the GOCPI Prototype as at Monday 19th of October.
Created a Web-based interface on my personal website. I used my personal website as I purchased a domain name for additional purposes outside the scope of the project.
Created a pipeline to continue developing the GOCPI prototype.

## Slide 15: Pursuing GOCPI’s Full Potential
Continue developing Australia and New Zealand energy system example.
Adopt new forecasting methodologies to project the needs of energy systems in the future. These include methods common in financial services and data science.
Make adjustments to the objective function to account for emissions and carbon taxes.
Continue to develop GOCPI classes to improve usability and convert the OseMOSYS model to Python to utilise IBM Watson Machine Learning and Cloud services.
Create user interfaces to display the outputs of energy systems and make comparisons to align with the United Nation’s Sustainable Development Goals (UNSDG) and Paris Agreements.